## Slide 1: Pycroscopy Data Formatting
Stephen Jesse, Suhas Somnath, Chris Smith
01/30/2017

## Slide 2: SPM Data Formatting and Analysis Efforts at CNMS
Data Format:
  Data stored in HDF5 format
    Open source format. Hierarchical Data Format v5 (HDF5)
  Same standard for different microscopes and microscopy methods
  Works for standard imaging and spectroscopic measurements as well
    Conventional AFM images would have a single data point at each spatial location. Eg – tapping mode imaging, contact mode imaging
    Spectral images : One or more parameters systematically varied over a range of values at different spatial positions in a grid or cloud of points. Example – band excitation data

## Slide 3: What is an HDF5 File?
An HDF5 file is a smart container
  Hierarchical / tree structure
  Capable of storing:
    Multidimensional datasets
    Images
    text
  Contents organized like traditional folders and files
  Important components:
    Datagroup - Analogous to folders in a file system
    Dataset – contains 1 to N dimensional data
      Integer, floating point, complex numbers etc
    Attributes – Key : value pairs that contain information to describe the data. Eg – units.
    References – Analogous to shortcuts / links
See here for more information on HDF5: http://extremecomputingtraining.anl.gov/files/2015/03/HDF5-Intro-aug7-130.pdf

## Slide 4: Data Formatting – Main Datasets
All data, regardless of dimension, is laid out into a 2D array
The first dimension for location index
The second dimension for spectral index
Keys provide instructions on original data dimensionality
Allows for irregular position arrays (cloud of points)
Allows for irregular spectral measurements (set-pulses,…)
Keeps track measurement sequence
Format matches what PCA, ICA, etc. expects

## Slide 5
HDF5 File Format for BE: Ver. 4
Root
Measurement conditions 1
Group
If measurement conditions change (e.g. adjustments to the band width or center) during a measurement, a new folder within the full data set will be created. Presumably this will not happen often.
Measurement conditions 2
Attribute A
Attribute Z
…
Contains top level attributes
2D Matrix for an Entire Spectral-Image Chunked by outermost position loop.
These results have been already normalized by the excitation band
Index matrix of instances
value matrix of instances
Frequency index
Value matrix for observables
Cycle index
1D time vector of excitation
Note:
This example represents 5D data:
3 spatial dimensions
2 spectral dimension
Normalization matrix
Position Matrices

## Slide 6: Data Formatting – Cont.
All data, regardless of dimension, is laid out into a 2D array
The first dimension for location index
The second dimension for spectral index
Keys provide instructions on original data dimensionality
Allows for irregular position arrays (cloud of points)
Allows for irregular spectral measurements (set-pulses,…)
Keeps track measurement sequence
Format matches what PCA, ICA, etc. expects
Subsequent analysis, such as fitting, is contained in ‘subfolders’
of the parent data within the HDF5 structure

## Slide 7: HDF5 File Format for BE: Ver. 4
Root
Measurement conditions 1
Group
Measurement conditions 2
SHO Fit Results, Measurement conditions 1 - subGroup
Fitting results (and fit guesses) get their own group within the parent data group.
References to fit procedures are contained in attributes.
Adoption of new fit parameter indices reflects dimensionality reduction.
Continue to share location indices with the parent data.
Attribute A
Attribute Z
…
Parent data
SHO Fit results matrix
SHO Fit guess matrix
UDVS index
Fit parameter index

## Slide 8: Example Datafile
Datasets link to relevant ancillary data
Data columns / rows can be accessed by name instead of indices
Metadata stored as attributes
Nomenclature of datagroups provides simple way to understand sequence of steps applied to process data

## Slide 9: Generic File Rules – Mandatory Datasets
<Root>
  Measurement_000 (new measurement group each time parameters change)
    Channel_000 (one for each physical channel like deflection, lateral.. All channels should be recorded simultaneously.)
      <Raw_Data> (positions x time or spectroscopic values)
        type : uint8, float32, complex64 etc.
        Required attributes:
          Position_Indices – HDF5 Object reference to the <Position_Indices> Dataset
          Position_Values – HDF5 Object reference to the <Position_Values> Dataset
          Spectroscopic_Indices – HDF5 Object reference to the <Spectroscopic_Indices> Dataset
          Spectroscopic_Values – HDF5 Object reference to the <Spectroscopic_Values> Dataset
          Quantity - Single string that explains the data – eg – Current or Voltage
          units – list of a single string for units like nA, V, F, etc.
          Region references that match those in the <Position_Indices> Dataset
          Region references that match those in the <Spectroscopi_Indices> Dataset
      <Position_Indices> (positions x spatial dimensions)
        type : uint32
        Required attributes:
          labels - list of strings for the column names
          Region references based on column names
      <Position_Values> (positions x spatial dimensions)
        type : float32
        Required attributes:
          labels - list of strings for the column names
          units – list of strings for units like nm / um
          Region references based on column names
      <Spectroscopic_Indices> (spectroscopic parameter x spectroscopic indices)
        type : uint32
        Required attributes:
          labels - list of strings for the row names
          Region references based on row names
      <Spectroscopic_Values> (spectroscopic parameter x spectroscopic values)
        type : (at least) float32 or complex64
        Required attributes:
          labels - list of strings for the row names
          units – list of strings for units like mV / rad / sec
          Region references based on row names
  Measurement_001…
Legend:
Dataset
Datagroup
Attribute
Additional datasets, data groups, and attributes can be added as necessary depending on the measurement

## Slide 10: Generic SPM File Rules – Attributes for Root
<Root>:
  comments = ’10X amplifier used’
  data_tool = ‘be_analyzer’
  data_type = ‘BELine’  mandatory – used for reading data
  experiment_date = 2015_10_15-14_55_05
  experiment_unix_time = 1.35654765E+9
  microscope = ‘Asylum Research Cypher’
  instrument = ‘Cypher West CNMS’
  project_id = ‘CNMS_2015B_X0252’
  project_name = ‘HfO2 investigation’
  sample_description = ‘8 nm HfO2 with 300um2 capacitors’
  sample_Name = ‘HFO2’
  translate_date = 2015_10_15-14_55_05
  translator = ‘ODF’
  user_name = ‘John Doe’
  xcams_id = ‘jdoe’
Incorporating units:
  attribute_name_[unit] = Value
  read_voltage_[V] = 3.9
Time stamp:
  YYYY_MM_DD-HH_mm_ss
  24 hour format for hours

## Slide 11: Nomenclature for Processing Tools
General Rule
DatasetName
DatasetName-ToolName_00x
  time_stamp
  machine_id
  tool_name
  algorithm
  Other relevant attributes
  ToolResult0
    Reference to DatasetName
    Reference to mapping matrices (position / spectroscopic) for unpacking and/or plotting
    labels
    units
  ToolResult1
    …..
Example -> Chain of analysis tools (SVD and kMeans)
Raw_Data
Raw_Data-SVD_000
  <SVD Attributes>
  S
    <Relevant references>
  U
    <Relevant references>
  V
    <Relevant references>
  U-Cluster_000
    Type = ‘KMeans’
    Labels
      <Relevant references>
    Mean_Response
      <Relevant references>
Raw_Data-SVD_001
  S
  U…
Legend:
Dataset
Datagroup
Attribute
Current methodology facilitates:
Same tool (with different parameters) to be applied to same dataset (different suffixes)
Tracing of all processing applied to any given dataset (using paths)
Analysis tools include function fitting, multivariate analysis functions etc. while processing tools include signal / image filtering, flattening functions etc.

## Slide 12: Example Rules for Processing Tool – Singular Value Decomposition (SVD)
Raw_Data
Raw_Data-SVD_000
  time_stamp
  machine_id
  tool_name
  algorithm
  S
  Component_Indices
  U
    Copy of the Position_Values attribute of Raw_Data
    Copy of the Position_Indices attribute of Raw_Data
    Reference to Component_Indices named as ‘Spectroscopic_Indices’
    Reference to S named as ‘Spectroscopic_Values’
    labels
    units
  V
    Reference to Component_Indices named as ‘Position_Indices’
    Reference to S named as ‘Position_Values’
    Copy of the Spectroscopic_Values attribute of Raw_Data
    Copy of the Spectroscopic_Indices attribute of Raw_Data
    labels
    units
Legend:
Dataset
Datagroup
Attribute
Do NOT store references to source dataset – Should the user want to only export a certain analysis / processing result (group), all the references within the group will also be copied over.